## Slide 1
- Compare three boundary treatments -
Soohwan Kim (ME PhD, Georgia Tech)
Lid-Driven Flow
in a Semi-Circular Cavity
using Lattice Boltzmann Method
Notes: You will learn some boundary treatment for curved geometry

## Slide 2
Motivations
(1) Advance our friendly problem
(2) Implement LBM in curved boundaries
Lattice configurations?
Bounce-back conditions?
U
L
L
U
L
L

## Slide 3
Former Studies
Rajan, I., & Perumal, D. A. (2021). Flow Dynamics Of Lid-Driven Cavities With Obstacles Of Various Shapes And Configurations Using The Lattice Boltzmann Method. Journal of Thermal Engineering, 7(2), 83-102.
Arun, S., & Satheesh, A. (2015). Analysis of flow behaviour in a two sided lid driven cavity using lattice boltzmann technique. Alexandria Engineering Journal, 54(4), 795-806.
All Re = 1000
- Two-sided lid driven cavity
- Obstacles with different geometries

## Slide 4
x
y
u = 1, v = 0
ur = 0, u = 0
u = 0, v = 0
Problem Description
Assumptions
- BGK collision operator
- D2Q9 model
- No slip, no penetration
- SRT model
- Incompressible
- Re = 100-1000
- Low Mach #

## Slide 5
Lattice configurations
Mei, R., Shyy, W., Yu, D., & Luo, L. S. (2000). Lattice Boltzmann method for 3-D flows with curved boundary. Journal of Computational Physics, 161(2), 680-699.
x
y
, = 1
,
,
2N
N

## Slide 6
Three Approaches
Staircase approximation
full-way bounce-back
Staircase approximation
half-way bounce-back
Interpolation
Li, Q., Yu, Y., & Luo, K. H. (2019). Implementation of contact angles in pseudopotential lattice Boltzmann simulations with curved boundaries. Physical Review E, 100(5), 053313.
Complexity & Accuracy

## Slide 7
Staircase Full-way Bounce-back
for three ’s
(e.g., 3,6,7 for south wall)
w
w
direction towards solid
direction towards fluid

## Slide 8
Staircase Half-way Bounce-back
b
f
direction towards solid
direction towards fluid
=
= 2, 3… 9 s.t. is solid node

## Slide 9
Interpolation Methods for Curved Boundary
Filippova and Hanel (1998) → Mei et al. (1999)
→ Bouzidi et al. (2001) → Yu et al. (2003)
1146
Filippova, O., & Hänel, D. (1998). Grid refinement for lattice-BGK models. Journal of computational Physics, 147(1), 219-228.
Mei, R., Luo, L. S., & Shyy, W. (1999). An accurate curved boundary treatment in the lattice Boltzmann method. Journal of computational physics, 155(2), 307-330.
Bouzidi, M. H., Firdaouss, M., & Lallemand, P. (2001). Momentum transfer of a Boltzmann-lattice fluid with boundaries. Physics of fluids, 13(11), 3452-3459.
Yu, D., Mei, R., Luo, L. S., & Shyy, W. (2003). Viscous flow computations with the method of lattice Boltzmann equation. Progress in Aerospace sciences, 39(5), 329-367.
1320
783
citations: 846
Notes: I did not take a close look at the derivation of these equations but just use them to recreate in my coding
I took a look at some review papers
Farrokhpanah, A., Nabovati, A., & Mostaghimi, J. (2014). Study of curved boundary treatments in lattice Boltzmann method. In Proceedings of The Canadian Society for Mechanical Engineering International Congress.

## Slide 10
Interpolation Method (Yu et al.)
Yu, D., Mei, R., Luo, L. S., & Shyy, W. (2003). Viscous flow computations with the method of lattice Boltzmann equation. Progress in Aerospace sciences, 39(5), 329-367.
direction towards solid
direction towards fluid
After streaming, we have and ,
Linear interpolation:
Momentum balance: ( = 0 in fixed wall)
Linear interpolation:
~ ~ ~
~
Notes: direction of the particle momentum moving

## Slide 11
Algorithm
Initialization
Collision
BC Treatment
Curved fixed wall
Flat moving wall
Reconstruction
Calculate
Calibrate for solid nodes
Reconstruction
Calculate 𝜌, 𝑢, 𝑣
Calibrate 𝜌,=𝜌_0 , 𝑢=0, 𝑣=0 for solid nodes
Streaming
Initialization
Collision
BC Treatment
Curved fixed wall
Flat moving wall
Streaming
Iteration
until norm of u < 10-5
Notes: Vorticity contour

## Slide 12
Results - Interpolation Method
Streamlines
u field
v field
N = 50
Re = 100
Notes: Vorticity contour
Half-way bounce back
This method gives second order
accuracy in simple geometries15 such as laminar flow
through parallel plates, but reduces to first order accuracy
in more complicated geometries.
Cosgrove, J. A., Buick, J. M., Tonge, S. J., Munro, C. G., Greated, C. A., & Campbell, D. M. (2003). Application of the lattice Boltzmann method to transition in oscillatory channel flow. Journal of Physics A: Mathematical and General, 36(10), 2609.
Chen, S., Martinez, D., & Mei, R. (1996). On boundary conditions in lattice Boltzmann methods. Physics of fluids, 8(9), 2527-2536.
He, X., Zou, Q., Luo, L. S., & Dembo, M. (1997). Analytic solutions of simple flows and analysis of nonslip boundary conditions for the lattice Boltzmann BGK model. Journal of Statistical Physics, 87(1), 115-136.

## Slide 13
Comparison with Square Cavity (Re = 100)
Streamlines
u profile (x/H = 0.2, 0.5, 0.8)
Notes: Vortex core location

## Slide 14
Comparison with Square Cavity (Re = 400)
Streamlines
u profile (x/H = 0.2, 0.5, 0.8)
Notes: Vortex core location

## Slide 15
Effects of Reynolds Number
Re = 100
Re = 400
Re = 1000
N = 50
Interpolation method
Re = 100 - 1000

## Slide 16
Results – Comparisons of Three Methods
Staircase approximation
full-way bounce-back
Staircase approximation
half-way bounce-back
Interpolation
Centerline u profile
N = 50
Re = 100

## Slide 17
Results – Convergence Comparison
# of iterations | Stair full | Stair half | Interpolation
1000 | 3.8 | 3.5 | 5.6
2000 | 6.6 | 6.6 | 10.8
↓ Time taken in seconds using MATLAB (Intel i5 processor)
N = 50
Re = 100
Ground-truth:
(N=250, Interpolation)
Centerline u profile
Notes: Re 100
1e-5 criteria
Full 7461-23.6s 2000-6.6s 1000- 3.8s 500-1.8s
Half 7475-23.0s 2000-6.6s 1000-3.5s 500-1.8s
Yu 8885-46.0s 2000-10.8s 1000-5.6s 500-2.9s

## Slide 18
RMS Error and Spatial Convergence Rate
Re = 100
Ground truth (N=250, interpolation)
RMS error with ground truth
N | 10 | 25 | 50 | 100
Full Bounce-back | unstable | 0.0136 | 0.0125 | 0.0121
Half Bounce-back | 0.0167 | 0.0135 | 0.0125 | 0.0121
Interpolation | 0.0170 | 0.0137 | 0.0126 | 0.0121
→ Interpolation is the most computationally heavy but all methods have similar levels of accuracy
Notes: N 10 25 50 100
Full unstable 0.0136 0.0125 0.0121
Half 0.0167 0.0135 0.0125 0.0121
Yu 0.0170 0.0137 0.0126 0.0121
Theoretically, D2Q9 method with explicit discretization has 2nd order convergence in space and time

## Slide 19
LBM without BC Implementation
Initialization
Collision
BC Treatment
Reconstruction
‘only’ in fluid nodes
(where isfluid = 1)
Streaming
Iteration
until norm of u < 10-5

## Slide 20
Other Ideas
U
U
Semi-circular cavity
without side walls
Circular cavity
with moving curved lid
U

## Slide 21
Comparison with Literatures
Migeon, C., Texier, A., & Pineau, G. (2000). Effects of lid-driven cavity shape on the flow establishment phase. Journal of Fluids and Structures, 14(4), 469-488.
Visualization (Re = 1000)
LBM (no BC)
Re = 400
Re = 1000
Notes: discrete solid tracers both coupled with a laser sheet illumination

## Slide 22
Conclusion
- Employed three schemes for curved boundary treatment :
(1) staircase approximation with full-way bounce-back,
(2) staircase approximation with half-way bounce-back,
(3) interpolation method suggested by Yu et al. (2003)
→ the interpolation is the most computationally heavy but other two methods showed decent accuracy
- LBM implementation within fluid nodes without BC treatment seems effective but may not convey the complete physics
(2) Implement LBM in curved boundaries